## Slide 1: Assembling an IoT Device
Presented by
Eng. NIYITEGEKA Janvier
RP/IPRC TUMBA

## Slide 2: What is an IoT Device?
A "Thing" can be any object that has a unique identifier and which can send/receive data over a network (e.g., smart phone, smartTV, computer, refrigerator, car, etc.).
• IoT device is a thing that can be connected to the Internet and send information about themselves or about their surroundings.

## Slide 3: Examples of an IoT device
A home automation device that allows remotely monitoring the status of appliances and controlling the appliances.
An industrial machine which sends information abouts its operation and health monitoring data to a server.
A car which sends information about its location to a cloud-based service.
A wireless-enabled wearable device that measures data about a person such as the number of steps walked and sends the data to a cloud-based service.

## Slide 4: IoT Device Requirements
Sensing Capability
Computation/Processing capability
Communication capability
Storage capability

## Slide 5: Components of an IoT Device
(i) I/ O interfaces for sensors,
(ii) interfaces for network/internet connectivity,
(iii) memory and storage interfaces
(iv) Processing device
(v) audio/ video interfaces.

## Slide 6: Device Platforms
Pycom Lopy
Raspberry Pi
microcontroller platforms:
Arduino Series
NodeMCU

## Slide 7: Hardware Interfaces
Universal Serial Bus (USB)
General-purpose input/output pins (GPIO)
GPIO pins can be digital or analog signals, and digital pins have only two states: HIGH or LOW.
Digital GPIO can support Pulse Width Modulation (PWM).

## Slide 8: Hardware Interfaces
Inter-Integrated Circuit (I2C): serial bus uses a protocol that enables multiple modules to be assigned a discrete address on the bus.
Universal Asynchronous Receiver/Transmitter (UART) devices translate data between serial and parallel forms at the point where the data is acted on by the processor
Serial Peripheral Interface (SPI.) bus devices employ master-slave architecture, with a single master and full-duplex communication.

## Slide 19: Basics of SPI

## Slide 20: SPI Configuration
Primarily used for serial communication between a host processor and peripherals.
Can also connect 2 processors via SPI
SPI works in a master slave configuration
The master being the host microcontroller for example and the slave being the peripheral

## Slide 21: SPI example

## Slide 22: SPI Operation
For SPI, there are Serial Clocks (SCLK), Chip Select lines (CS), Serial Data In (SDI) and Serial Data Out( SDO)
There is only one master, there number of slaves depends on the number of chip select lines of the master.
Synchronous operation, latch on rising or falling edge of clock, SDI on rising edge, SDO on falling edge
Operates in 1 to 2 MHz range
Master sends out clocks and chip selects. Activates the slaves it wants to communicate with

## Slide 23: Multiple Slaves Configuration

## Slide 24: Master Slave Setup
Multiple Independent Slave Configuration

## Slide 28: I2C example(gy-80,gy-251)

## Slide 30: Microcontroller Platforms

## Slide 31: Android Uno
ATMega328 chip and uses USB, AC/DC adapter or battery as power source
supports up to 12V power using a wall-wart adapter
14 digital input/output (I/O) pins and 6 analog input pins
Six of the digital I/O pins can be used as PWM.
The analog pins’ resolution is the maximum of 10 bits , delivering 1024 different reading values
8-bit CPU, 2KB SRAM, 32 KB flash memory, 1 KB EEPROM, 16MHz clock speed

## Slide 32: Arduino Nano
The Arduino Nano is a small, complete, and breadboard-friendly board based on the ATmega328P (Arduino Nano 3.x)
Flash Memory 32 KB of which 2 KB used by bootloader
SRAM 2 KB; Clock Speed 16 MHz
Analog IN Pins 8;EEPROM 1 KB
DC Current per I/O Pins 40 mA (I/O Pins)
Input Voltage 7-12V; Digital I/O Pins 22 (6 of which are PWM)
PWM Output 6
Power Consumption 19 mA.

## Slide 33: Arduino Nano Schematic

## Slide 34: NodeMCU Platform

## Slide 35: NodeMCU Platform

## Slide 36: Arduino Data Types

## Slide 37: Coding Fundamentals
Variables Type Variable = Value int pin = 14 pinMode(pin, OUTPUT)
int pin = 14\\Global dec void setup() {pinMode(pin, OUTPUT); }
void loop() {digitalWrite(pin, High)}

## Slide 38: Cont’d
digitalWrite(pin, value)
pinMode(pin, mode)-INPUT, OUTPUT
Serial.print(78, BIN) gives "1001110"
Serial.print(78, OCT) gives "116"
Serial.print(78, DEC) gives "78"
Serial.print(78, HEX) gives "4E"
Serial.println(1.23456, 0) gives "1"
Serial.println(1.23456, 2) gives "1.23"
Serial.println(1.23456, 4) gives "1.2346

## Slide 39: Function Reference

## Slide 40: Blinking Circuit

## Slide 41: SparkFun Barometric Pressure Sensor Breakout - BMP180
This is a breakout board for the Bosch BMP180 high-precision, low-power digital barometer.
BMP180 offers a pressure measuring range of 300 to 1100 hPa with an accuracy down to 0.02 hPa
piezo-resistive technology for high accuracy, ruggedness and long term stability
It connects to a microcontroller via I²C bus (also known as TWI, or on the Arduino, the "Wire" library).

## Slide 42: Cont’d
BMP180 measures absolute pressure. Since absolute pressure varies with altitude, you can use the pressure to determine your altitude.
The BMP180 measures both pressure and temperature, because temperature changes the density of gasses like air. At higher temperatures, air is not as dense and heavy, so it applies less pressure on the sensor. At lower temperatures, air is more dense and weighs more, so it exerts more pressure on the sensor
The SI unit - the Pascal (Pa). One Pascal is defined as one Newton of force per square meter. The BMP180 outputs pressure readings in Pascals, but they are converted to hectoPascals (hPa) by the software library .

## Slide 43: Reading pressure
SFE_BMP180 Library
startTemperature() and getTemperature()
startPressure() and getPressure()

## Slide 44: Neo-6M GPS to Arduino

## Slide 45: NEO-6M GPS Module

## Slide 46: Libraries
SoftwareSerial is a library of Arduino which enables serial data communication through other digital pins of Arduino.
The library replicates hardware functions and handles the task of serial communication.
TinyGPS is a library that converts all those NMEA messages into a readable format by stuffing the character sequences into variables.

## Slide 47: DS18B20 Water Proof temperature sensor
DS18B20 is 1-Wire digital temperature sensor from Maxim IC. Reports degrees in Celsius with 9 to 12-bit precision, from -55 to 125 (+/-0.5). Each sensor has a unique 64-Bit Serial number etched into it - allows for a huge number of sensors to be used on one data bus.
Unique 1-Wire® interface requires only one port pin for communication
Each device has a unique 64-bit serial code stored in an onboard ROM
Multidrop capability simplifies distributed temperature sensing applications
Requires no external components
Can be powered from data line.
Power supply range is 3.0V to 5.5V
Measures temperatures from –55°C to +125°C (–67°F to +257°F)±0.5°C accuracy from –10°C to +85°C
Thermometer resolution is user-selectable from 9 to 12 bits
Converts temperature to 12-bit digital word in 750ms (max.)
User-definable nonvolatile (NV) alarm settings
Alarm search command identifies and addresses devices whose temperature is outside of programmed limits (temperature alarm condition)
Applications include thermostatic controls, industrial systems, consumer products, thermometers, or any thermally sensitive system

## Slide 48: Connection
You will need a pull-up resistor of about 5 KOhm between the 1-Wire data line and your 5V power.

## Slide 49: DHT22 digital temperature and humidity sensor module
the DHT-22 is a digital humidity and temperature sensor. It uses a capacitive humidity sensor and a thermistor to measure the surrounding air, and spits out a digital signal on the data pin.
Power: 3-5V
Max Current: 2.5mA
Humidity: 0-100%, 2-5% accuracy
Temperature: -40 to 80°C, ±0.5°C accuracy
No more than 0.5 Hz sampling rate (once every 2 seconds)
Body size 15.1mm x 25mm x 7.7mm
4 pins with 0.1" spacing

## Slide 50: Library
https://github.com/adafruit/DHT-sensor-library

## Slide 51: Connection

## Slide 52: Capacitive Soil Moisture Sensor

## Slide 53: Raspberry Pi

## Slide 54: Raspberry Pi 2 Model B
It is actually a small computer, it runs Linux as operating system
It has a full network system, solving thus the processing problem of the Arduino.

## Slide 55: Raspberry Pi 2 Model B Pin out

## Slide 56: Raspberry pi peripherals

## Slide 57: Raspberry pi peripherals

## Slide 58: Pin out with MUX

## Slide 59: Raspberry pi Models

## Slide 60: Arduino & Raspberry pi

## Slide 61: Thank You!!!